## Slide 1
EMERTXE EMBEDDED SYSTEMS INTERNSHIP • CAPSTONE WALKTHROUGH
EV ADAS Dashboard
From a Single Blinking LED to a Real-Time ADAS + EV Telemetry System
STM32F103C8T6 Blue Pill
PicSimLab
STM32 HAL
Python + Matplotlib
UART @115200
Presented by Debjit Das • Animesh Kullu • Supradip Karmakar • B.Tech ECE, JGEC
Session format: PPT walkthrough + live PicSimLab simulation demo

## Slide 2
AGENDA
What This Walkthrough Covers
Four stages, mirroring how the firmware itself was actually built — one peripheral at a time.
01
Foundations
Toolchain, ARM/STM32 basics, first LED blink, timer interrupts
02
Signals & Sensing
ADC theory, 4-channel pedal/battery/temp sensing over UART
03
EV + ADAS Engine
Speed/SOC/regen physics model, HC-SR04 collision & blind-spot logic
04
Telemetry & Dashboard
UART protocol, shell commands, live Python matplotlib dashboard
EV ADAS Dashboard • Emertxe Embedded Systems Internship
2 / 26

## Slide 3
MOTIVATION
Why Build a Smart EV Dashboard?
THE PROBLEM
Modern EVs generate huge volumes of real-time sensor data — speed, battery SOC, motor temperature, torque, and range.
Without a centralized dashboard, engineers cannot monitor EV performance and ADAS safety data simultaneously.
A single operator cannot track everything manually — collisions, blind spots, and faults can go undetected.
OUR SOLUTION
Real-time speed, SOC & range monitoring
ADAS collision & blind-spot detection
Motor temperature & fault alerting
Live Python dashboard streamed over UART
Tiered alarm system (Advisory → Critical)
Drive-mode control (ECO / NORMAL / SPORT)
EV ADAS Dashboard • Emertxe Embedded Systems Internship
3 / 26

## Slide 4
FOUNDATIONS · 01
Development Environment & Tools
HOST vs TARGET
Host: Laptop running STM32CubeIDE — where firmware is written & built
Target: PicSimLab → simulates a Blue Pill board → STM32F103C8T6 MCU
WHY SIMULATE FIRST?
PicSimLab models real GPIO/ADC/UART/timer behaviour in software — letting the whole firmware stack (blink → sensors → EV physics → ADAS → dashboard) be built, tested, and demoed without any physical hardware on the bench.
Software | Purpose
STM32CubeIDE | STM32 firmware programming (CubeMX config + build + flash)
PicSimLab | STM32 Blue Pill board simulation — GPIO, ADC, UART, timers
Python 3 + pip | Runs the dashboard application and its libraries
matplotlib, numpy | Live 10 fps gauge / chart visualization
pyserial | Reads the UART telemetry stream from PicSimLab's virtual COM port
Software
Purpose
EV ADAS Dashboard • Emertxe Embedded Systems Internship
4 / 26

## Slide 5
FOUNDATIONS · 02
ARM Cortex-M & the STM32F103
95%+
of smartphones run on ARM cores
200+
silicon vendors license ARM
30B+
ARM chips shipped in 2023 alone
Blue Pill = STM32F103C8T6
Cortex-M3 core · up to 72 MHz · 64 KB Flash · 20 KB SRAM · low-cost, general-purpose — best for LED / sensor / communication projects like this one.
Application
Cortex-A
High performance · runs Linux/Android — phones, tablets
Real-Time
Cortex-R
Deterministic · safety-critical — automotive ECUs, medical
Microcontroller
Cortex-M
Low power, low cost — IoT, sensors, embedded control
Cortex-M SERIES — increasing performance & power →
M0 / M0+
Smallest, most energy efficient — ultra-low-power IoT
M3 (used here)
General-purpose, no DSP/FPU — STM32F1 family
M4
DSP + optional FPU — signal processing, STM32F4
M7
High performance — dual-issue, large cache
EV ADAS Dashboard • Emertxe Embedded Systems Internship
5 / 26

## Slide 6
FOUNDATIONS · 03 — DAY 1
First Blink: Plain GPIO Toggle
Every board bring-up starts the same way — prove the toolchain, the flash, and one pin all work together.
main.c — while(1) loop
GPIO_InitStruct.Pin = GPIO_PIN_13;
GPIO_InitStruct.Mode = GPIO_MODE_OUTPUT_PP;
HAL_GPIO_Init(GPIOC, &GPIO_InitStruct);
while (1)
{
HAL_GPIO_TogglePin(GPIOC, GPIO_PIN_13);
HAL_Delay(500);
}
KEY HAL CALLS
HAL_GPIO_WritePin()
Drives a pin explicitly SET or RESET
HAL_GPIO_TogglePin()
Inverts the current output state
HAL_Delay(ms)
Blocking millisecond delay (SysTick-based)
PC13 IS ACTIVE-LOW
On Blue Pill boards, PC13 drives the onboard LED to ground — the pin is lit when driven LOW. A toggle still blinks correctly either way; only the very first visible state depends on the initial output level.
EV ADAS Dashboard • Emertxe Embedded Systems Internship
6 / 26

## Slide 7
FOUNDATIONS · 04 — DAY 2
Non-Blocking Blink: TIM1 Interrupt
HAL_Delay() ties up the CPU. Swapping to a hardware timer interrupt frees the processor for everything that comes later.
Update Frequency = TIM1_CLK / [ (PSC+1) × (ARR+1) ]
PSC = 7199, ARR = 9999 → divisor = 7200 × 10000 = 72,000,000
TIM1_CLK
72,000,000 Hz (typical Blue Pill default)
Update Frequency
72,000,000 / 72,000,000 = 1 Hz
LED toggle rate
Every 1 s → full ON/OFF cycle = 2 s
Why this matters later: the exact same pattern — configure a timer, enable its interrupt, act in the callback — later drives the 10 ms EV-physics tick (TIM1) and the 100 ms sensor tick (TIM3).
Generated + user code
htim1.Instance = TIM1;
htim1.Init.Prescaler = 7199;
htim1.Init.Period = 9999;
HAL_TIM_Base_Init(&htim1);
/* USER CODE 2 */
HAL_TIM_Base_Start_IT(&htim1);
void HAL_TIM_PeriodElapsedCallback(
TIM_HandleTypeDef *htim)
{
if (htim->Instance == TIM1)
HAL_GPIO_TogglePin(GPIOC,
GPIO_PIN_13);
}
EV ADAS Dashboard • Emertxe Embedded Systems Internship
7 / 26

## Slide 8
SIGNALS & SENSING · 05
ADC Fundamentals: 12-bit Mapping
ADC Value = ( Vin / Vref ) × 4095 Voltage = ADC_Value × 3.3 / 4095
0.0 V
0
0% — pedal released
1.65 V
2047
50% — mid-range
3.3 V
4095
100% — pedal floored
STM32F103 ADC FACTS
Resolution: 12-bit (0 – 4095)
Vref: 0 – 3.3 V
Up to 18 channels · Single / Scan / Continuous modes
COMMON MISTAKE
PicSimLab's ADC does NOT support Scan/DMA multi-channel. Every channel must be read one at a time by calling HAL_ADC_ConfigChannel() before each HAL_ADC_Start().
EV ADAS Dashboard • Emertxe Embedded Systems Internship
8 / 26

## Slide 9
SIGNALS & SENSING · 06
Polling 4 Channels → UART Display
Channel | Pin | Signal
IN0 | PA0 | Accelerator Pedal
IN1 | PA1 | Brake Pedal
IN2 | PA2 | Battery SOC
IN3 | PA3 | Motor Temp
Channel
Pin
Signal
EXECUTION ORDER (each loop)
PA0 Accel
→
PA1 Brake
→
PA2 SOC
→
PA3 Temp
→
UART TX
Scaling: accel/brake/SOC = raw × 100/4095 (%) · temp = raw × 150/4095 (0–150°C)
ADC_Read() helper
cfg.Channel = channel;
cfg.Rank = ADC_REGULAR_RANK_1;
HAL_ADC_ConfigChannel(&hadc1,&cfg);
HAL_ADC_Start(&hadc1);
HAL_ADC_PollForConversion(&hadc1,100);
val = HAL_ADC_GetValue(&hadc1);
HAL_ADC_Stop(&hadc1);
UART OUTPUT · 115200 baud, 8N1
ACCEL= 45% BRAKE= 0%
SOC = 78% TEMP = 65C
Don't use printf() directly — it needs retargeting. Build the string with sprintf() and send it via HAL_UART_Transmit().
EV ADAS Dashboard • Emertxe Embedded Systems Internship
9 / 26

## Slide 10
SYSTEM DESIGN · 07
System Architecture & Pin Map
Sensors
Potentiometers
(Accel/Brake/SOC/Temp)
+ 3× HC-SR04
→
STM32 Blue Pill
EV Control · ADAS Engine
· Fault Handler
→
UART · 115200 bps
Structured telemetry
frames, every 100 ms
→
Python Dashboard
Speedometer · SOC bar
· ADAS bird's-eye view
KEY PIN ASSIGNMENTS — Blue Pill (STM32F103C8T6)
PA0–PA3 | ADC1 CH0–CH3 | Accel / Brake / SOC / Motor Temp
PA8 | TIM1 CH1 (PWM) | Motor drive signal, 20 kHz
PA9 / PA10 | USART1 TX / RX | Dashboard stream / command shell
PB0–PB5 | GPIO Trig/Echo | 3× HC-SR04: Front, Left, Right
PB8–PB11 | GPIO Output | Collision, blind-spot & fault LEDs
PC13 | GPIO Output | Repurposed: Day-1/2 blink LED → alarm buzzer (buzzer.c)
EV ADAS Dashboard • Emertxe Embedded Systems Internship
10 / 26

## Slide 11
EV + ADAS ENGINE · 08
EV Control Module — ev_control.c/.h
State Data
speed_kmh
torque_Nm
soc_pct (0–100%)
range_km
power_kW
mode, regen_active
Key Constants
MAX_SPEED = 200 km/h
MAX_TORQUE = 150 Nm
REGEN_MAX = −80 Nm
BRAKE_THRESH = 5%
DRAG_COEFF = 2.0
MASS_FACTOR = 100
Public Functions
EV_Init()
EV_Update()
EV_ReadADC()
EV_SetDriveMode()
EV_InjectSpeed()
EV_InjectSOC/Temp()
This one module quietly powers speed, battery drain, range, drive-mode feel, and regen braking — all from four HAL inputs.
EV ADAS Dashboard • Emertxe Embedded Systems Internship
11 / 26

## Slide 12
EV + ADAS ENGINE · 09
Speed Model — Lumped Inertia (Euler Step)
accel = (motor_torque − drag_Nm) / MASS_FACTOR speed_kmh += accel × dt × 3.6 [clamped 0–200]
motor_torque
Commanded torque (Nm), from throttle × MAX_TORQUE × mode_scale; negative during regen
drag_Nm
speed_ms × DRAG_COEFF — linear approximation of aero + rolling resistance
MASS_FACTOR
Tuned inertia/gearing constant = 100 — chosen for a punchy feel: full throttle gives ~1.5 m/s² in NORMAL, ~1.95 m/s² in SPORT
MOTOR POWER vs SPEED (NORMAL mode, τ = 150 Nm)
Chart: 
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200
Total (mech + loss) | 5 | 6 | 7 | 8 | 9 | 10.5 | 11.7 | 12.9 | 14 | 15 | 16.1
P_mech only | 0 | 1.1 | 2.2 | 3.3 | 4.4 | 5.5 | 6.6 | 7.8 | 8.9 | 10 | 11.1
CLAMP
Bounds check — CLAMP(v, 0, 200 km/h) — prevents negative speed and enforces the simulated top speed.
float speed_ms = speed_kmh / 3.6f;
float drag_Nm = speed_ms * DRAG_COEFF;
speed_kmh = CLAMP(speed_kmh + accel*dt*3.6f, 0.0f, MAX_SPEED_KMH);
EV ADAS Dashboard • Emertxe Embedded Systems Internship
12 / 26

## Slide 13
EV + ADAS ENGINE · 10
SOC Estimation, Range & Drive Modes
ΔSOC = (P_kW × dt) / (CAP_kWh × 3600) × 100 × SIM_SCALE
Copper-loss term (∝ torque²) means SOC still drains ~5 kW at standstill — models real motor current draw.
EV_SIM_SCALE — demo tuning for a full drain:
1.0
~2.7 hrs (real-time)
32.0
~5 minutes
160.0
~1 minute
DRIVE MODE × TORQUE SCALE
ECO × 0.6
90 Nm peak
NORMAL × 1.0
150 Nm peak
SPORT × 1.3
195 Nm peak
Range (km) = (SOC% / 100) × E_battery_kWh / η_mode × km_per_kWh
ESTIMATED RANGE BY DRIVE MODE (km)
Chart: 
| ECO | NORMAL | SPORT
Range | 210 | 160 | 123
EV ADAS Dashboard • Emertxe Embedded Systems Internship
13 / 26

## Slide 14
EV + ADAS ENGINE · 11
Regenerative Braking & Motor Thermal Model
REGENERATIVE BRAKING
Read brake pedal ADC (0–100%)
If brake% > REGEN_THRESHOLD (5%)...
regen_level = brake_pedal × 0.7 (0–70% scale)
motor_torque = −(regen_level/100) × REGEN_MAX_NM (80)
At 100% brake → torque = −0.7 × 80 = −56 Nm
Negative torque → negative power → SOC increases
Chart: Regen Torque vs Brake Pedal %
| 0% | 10% | 20% | 30% | 40% | 50% | 60% | 70% | 80% | 90% | 100%
Motor torque (Nm) | 0 | -5.6 | -11.2 | -16.8 | -22.4 | -28 | -33.6 | -39.2 | -44.8 | -50.4 | -56
MOTOR THERMAL MODEL
dT/dt = |P_kW|×0.05 − (T−25)×0.01
Heat Input
|P_kW| × 0.05 — 5% of motor power converted to heat, during power draw and regen alike
Cooling Term
(T − 25) × 0.01 — Newton's law of cooling, proportional to temp above 25°C ambient
Clamp
Result held within [25°C, 130°C] — 130°C also feeds the FAULT_OT trigger
EV ADAS Dashboard • Emertxe Embedded Systems Internship
14 / 26

## Slide 15
EV + ADAS ENGINE · 12
Ultrasonic ADAS Engine — 3× HC-SR04
SENSOR LAYOUT (BIRD'S-EYE)
FRONT
EV
LEFT
RIGHT
FCW Warning: < 50 cm · Critical: < 20 cm
Blind spot active: < 30 cm & speed > 20 km/h
TTC Warning: < 3.0 s · Critical: < 1.5 s
Sensor | Trigger → Echo | Zone / Trigger
Front | HC-SR04, GPIO poll | Forward collision warning + TTC calc
Left | HC-SR04, GPIO poll | Blind-spot detection (speed > 20 km/h)
Right | HC-SR04, GPIO poll | Blind-spot detection (speed > 20 km/h)
Sensor
Trigger → Echo
Zone / Trigger
Trigger → Echo Timing (per sensor)
1. Pulse TRIG high for 10 µs
2. Wait for ECHO to go high (start = counter)
3. Wait for ECHO to go low (stop = counter)
4. distance_cm = (stop−start) × 0.0343 / 2
5. 30 ms timeout guards against a
non-responding sensor in simulation
EV ADAS Dashboard • Emertxe Embedded Systems Internship
15 / 26

## Slide 16
EV + ADAS ENGINE · 13
ADAS Features Implemented
FCW
Forward Collision Warning
Grades obstacle proximity into 3 levels with a 3-sample hysteresis counter to stop rapid alarm toggling.
TTC
Time-To-Collision
TTC = distance / relative speed. Triggers WARNING under 3 s, CRITICAL under 1.5 s.
BSD
Blind Spot Detection
Left/right sensors active above 20 km/h; LED + alarm when a vehicle is detected within 30 cm.
PA
Parking Assist
Proximity score 0–100 from the average of all 3 sensors when speed drops below 10 km/h.
OS
Overspeed Advisory
ALARM_ADVISORY fires above 120 km/h, independent of obstacle state.
EV ADAS Dashboard • Emertxe Embedded Systems Internship
16 / 26

## Slide 17
SAFETY · 14
Fault Detection & 4-Level Alarm Priority
FAULT BIT-FIELD REGISTER (uint8_t)
Bit | Fault | Trigger
0 | FAULT_OT | Motor temp > 90°C
1 | FAULT_SOC | Battery SOC < 2%
2 | FAULT_COL | Collision critical (<20cm)
3 | FAULT_SEN | Reserved — sensor timeout (not yet wired)
4 | FAULT_COM | Reserved — comm timeout (not yet wired)
Bit
Fault
Trigger
Currently implemented in Fault_Check(): FAULT_OT, FAULT_SOC, FAULT_COL — packed as one hex byte (e.g. 0x04). On any fault: torque → 0, state → FAULT, red LED (PB11) latches.
4-LEVEL ALARM PRIORITY
P0 · NONE
Normal operation — no alerts active.
P1 · ADVISORY
Blind spot detected, or vehicle over 120 km/h.
P2 · WARNING
Collision < 50 cm, or TTC < 3 s.
P3 · CRITICAL
Collision < 20 cm, or TTC < 1.5 s — dashboard flashes red.
BUZZER OUTPUT — buzzer.c (PC13, non-blocking state machine)
P1 ADVISORY → SINGLE beep (150ms on / 850ms off) · P2 WARNING → DOUBLE beep (120/200ms) · P3 CRITICAL → RAPID beep (80/80ms)
PC13 has no timer channel on the F103, so tone is on/off cadence only — ticked from Buzzer_Process() each main-loop pass, never HAL_Delay().
EV ADAS Dashboard • Emertxe Embedded Systems Internship
17 / 26

## Slide 18
SAFETY · 15
Vehicle State Machine
PARKED
Enter: Power-on / reset
Exit: Accel > 2%
→
READY
Enter: Accel pedal > 2%
Exit: Immediate (next tick)
→
DRIVING
Enter: Automatic fall-through
Exit: Brake > 5%, or fault flagged
→
REGEN
Enter: Brake > 5% while driving
Exit: Brake < 5%
→
FAULT
Enter: Overheat / low SOC / collision
Exit: Auto-clears, or “fault clear”
All outputs off, UART heartbeat
Motor armed, sensors active
Motor PWM, ADAS active, streaming
Negative torque PWM, SOC charging
Cut PWM, open contactors, alarm
ALARM HYSTERESIS
An alarm only de-asserts once the triggering condition has been absent for 3 consecutive sensor readings (300 ms). This prevents rapid alarm toggling caused by noisy ultrasonic readings near a threshold, and applies to all P1–P3 alarm conditions.
EV ADAS Dashboard • Emertxe Embedded Systems Internship
18 / 26

## Slide 19
TELEMETRY & DASHBOARD · 16
UART Telemetry Protocol
115200 bps · two structured ASCII frames streamed every 100 ms
LINE 1 — EV TELEMETRY FRAME
SPD:72.5 SOC:79.3 TRQ:75 TMP:27.1 RNG:2600 ACC:50 BRK:0
LINE 2 — ADAS FRAME
F:40 L:400 R:400 TTC:2.1s COL:1 BSD:10 ALM:2 FLT:00
SPD
Speed km/h
SOC
State of charge %
TRQ
Motor torque Nm
TMP
Motor temp °C
RNG
Est. range (km)
F/L/R
Ultrasonic dist. cm
TTC
Time-to-collision (s)
ALM
Alarm priority 0–3
FLT
Fault byte (hex)
EV ADAS Dashboard • Emertxe Embedded Systems Internship
19 / 26

## Slide 20
TELEMETRY & DASHBOARD · 17
UART Shell — Live Parameter Injection
WHY A SHELL?
Inject exact speed/SOC values for deterministic testing
Validate alarm thresholds without dragging potentiometers
Simulate battery drain, overheat, and fault conditions
Switch drive modes over the serial terminal
Reset faults and observe recovery behaviour
speed set <kmh> | Set vehicle speed directly
soc set <pct> | Set battery state of charge
temp set <degC> | Set motor temperature
mode <eco¦normal¦sport> | eco / normal / sport
fault inject <motor¦soc¦col> | Injects motor overheat, low SOC, or collision
fault clear | Clear all faults, restore normal state
status | Print current EV + ADAS state summary
Also: obstacle <cm> / obstacle clear (override front sensor) · alarm test (cycles all 3 buzzer patterns) · reset · help
Command
Effect
EV ADAS Dashboard • Emertxe Embedded Systems Internship
20 / 26

## Slide 21
TELEMETRY & DASHBOARD · 18
Python Matplotlib Dashboard — 10 fps
Speedometer
Circular arc gauge 0–200 km/h. Colour green → orange → red with a needle + numeric readout.
Battery (SOC)
Horizontal bar with live % and estimated range; drive-mode badge shown below.
Speed History
60-sample rolling line chart, cyan trace on a dark background, 0–220 km/h.
EV Metrics
Info panel: torque, accel/brake %, motor temp, alarm level, fault code, UART status.
ADAS Bird's-Eye
Top-down view: ego vehicle, colour-coded front obstacle, BSD boxes, TTC label.
RUN IT
python dashboard.py
--port COM3
python dashboard.py --demo
COLOUR CODING
Normal / clear
Warning
Critical / fault
Ego vehicle
EV ADAS Dashboard • Emertxe Embedded Systems Internship
21 / 26

## Slide 22
RECAP
The Journey — 9 Build Phases
1
Dev Environment
STM32CubeIDE + PicSimLab + Python setup
2
GPIO & Peripherals
LED, PWM buzzer, timer interrupts (TIM1/3/4)
3
ADC Sensor Inputs
Potentiometers → accel, brake, motor temp
4
EV Dynamics Model
Speed, torque, SOC, range, regen, drive modes
5
Ultrasonic ADAS
HC-SR04 front/left/right → FCW + BSD + TTC
6
Fault & Alarm System
Bit-field faults + 4-level alarm priority
7
UART Telemetry
Structured frames: SPD / SOC / TRQ / TMP / RNG
8
UART Shell
Live parameter injection via serial commands
9
Python Dashboard
Matplotlib: speedometer, ADAS bird's-eye, SOC bar
EV ADAS Dashboard • Emertxe Embedded Systems Internship
22 / 26

## Slide 23
OUTCOMES
Results & What We Validated
Real-Time Speed & SOC
Speedometer updates at 10 fps; SOC drains correctly with power draw and recovers under regen braking.
ADAS Collision Detection
Front obstacle reliably detected below 50 cm; alarm escalates to CRITICAL at 20 cm with a dashboard red-flash.
Blind Spot Monitoring
Left/right BSD triggers above 20 km/h with correct 3-sample hysteresis — no false positives at highway speed.
Motor Over-Temp Fault
FAULT_OT (0x01) sets above 90°C; torque drops to 0, state → FAULT, LED latches ON.
Python Dashboard
All 5 panels render live from the UART stream; a --demo mode runs without hardware for presentation.
UART Shell Tested
speed set / fault inject / fault clear verified on the PicSimLab serial monitor; faults recover cleanly.
EV ADAS Dashboard • Emertxe Embedded Systems Internship
23 / 26

## Slide 24
SWITCHING TO SCREEN RECORDING
Live Simulation Demo
PicSimLab (Blue Pill) → UART → Python Dashboard, running live
EV ADAS Dashboard • Live Demo
24 / 26
EV ADAS Dashboard • Emertxe Embedded Systems Internship

## Slide 25
REFLECTION
Key Takeaways — Skills Gained
HAL Peripheral Programming
GPIO, ADC, Timers, UART — from register concepts to portable HAL calls
Interrupt-Driven Design
Moving from blocking HAL_Delay() loops to timer ISRs and multi-rate scheduling
Signal Processing
12-bit ADC mapping, scaling, and multi-channel polling under simulator constraints
Physics-Based Modelling
Inertia, drag, copper loss, and Newton cooling turned into real-time C code
Sensor Fusion for ADAS
Combining 3 ultrasonic sensors with speed data into TTC-based collision logic
Fault-Tolerant State Machines
Bit-field faults, hysteresis, and a deterministic 5-state vehicle lifecycle
Serial Protocol Design
A structured, parseable UART telemetry format plus a debug command shell
Real-Time Visualization
Streaming sensor data into a responsive 10 fps Python/matplotlib dashboard
EV ADAS Dashboard • Emertxe Embedded Systems Internship
25 / 26

## Slide 26
THANK YOU
EV ADAS Dashboard — STM32 Blue Pill · PicSimLab · Python
Emertxe Embedded Systems Internship — Capstone Project
Debjit Das · Team Emertxe
Animesh Kullu · Team Emertxe
Supradip Karmakar · Team Emertxe
Questions welcome